## Slide 1: Digital Twin System for Automotive Safety with Integration of a Safety Controller
Pruthvi Krishnamurthy
MSc Automotive Technology, MDSE
Notes: Good Morning
Thanks for being here for my presentation
My research topic is
It combines digital and automotive safety and testing

## Slide 2: Table of Contents
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: Before we dive into main content
Let me give an overview of the sections that we’ll be covering

## Slide 3: How confident are you about your car’s reliability ?
Why?
Extensive Physical Tests as per Standards and Regulation
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: Pretty confident right ?

## Slide 4: Testing for Advanced Systems
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
For features like Advanced Driver-Assistance System (ADAS) requires more special tests:
Automatic Emergency Braking
Lane Assist
Adaptive Cruise Control
Automatic Parking
We need to create suitable scenarios
Notes: Explain ADAS
Requires special setups and scenarios

## Slide 5: Drawbacks of Modern Testing
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Expensive (Special setups)
Time consuming
Resource intensive
Tedious for multiple iterations
Requires controlled environment

## Slide 6: Why this Project ?
    How Automotive Industry can improve testing methods
    Actual Human -> Crash Dummy -> Digital Twin
    Hazard Analysis & Risk Assessment scenarios
    Using virtual sensors
    Minimize Testing & Verification costs
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: physical testing consume more time, resources, and money
20 to 30 percent of development cost is spent on testing and validation and the shift towards virtualization reduces the cost and time.
The Digital Twin System can be a solution to this by stimulating these scenarios in a reliable virtual environment before physical testing to accelerate the development process

## Slide 7: Research Questions
1. How an Automotive System can be designed with Safety mechanisms?
2. How can virtual sensors be used instead of physical sensors?
3. How a Safety Controller can be integrated into the Hardware-in-loop (HIL) setup?
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
How a Digital Twin System can be integrated with a Safety Controller?
4. How the Digital Twin System’s performance can be optimized?

## Slide 8: Digital Twin
    Virtual + Physical Twin
    Communication
    Data
    Virtual replica of Physical Twin
Digital Twin System
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works

## Slide 9: Digital Twin System (DTS)
Physical entity, Virtual entity, Service system and Digital twin Data
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Service System
Digital Twin Data
Physical Entity
Virtual Entity
[Ref:Dynamic analysis of digital twin system based on five-dimensional model]
Notes: physical entity or the physical twin, the virtual entity or the digital twin, the service system, the digital twin data, and the connection.
the digital twin system is a dynamic system
The service system is an operational platform with input and output functions. Its workflow is: read data from external objects- form a database- make operational decisions- modify the database.

## Slide 10: Virtual Twin
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Comparison of Simulators
Y: Yes, N: No, U: Unknown
    Why CAR Learning to Act (CARLA) ?
[Ref:A survey on simulators for testing self-driving cars]
Notes: CarSim – Cars
Prescan – 3D environments
Gazebo – Robots
LGSVL – Unity Game Engine
CARLA – Unreal Engine
Requirement - the simulator should be capable of simulating autonomous vehicles, and support scenario based testing, and compatible with ROS environment.

## Slide 11: Digital Twin System (DTS) Communication
Virtual Sensors
Virtual Actuators
Physical ECU
ROS
ROS
CAN
CAN
Sensor data
Sensor data
Control Commands
Control Commands
MATLAB Simulink
Digital Twin (CARLA)
Physical Sensors
Physical Actuators
Physical Twin (Scaled Race Car)
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Digital Twin (CARLA)
Notes: Explain ROS and CAN as
communication protocol
ROS – Robotic applications
CAN – ECU communication

## Slide 12: Block Diagram for DTS
Data from DTS
Concept System Design
Perform Safety Analysis
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works

## Slide 13: V-Model Framework using Digital Twin System
System Concept Development
System
Requirements
System
Development & Implementation
Perform Safety
Analysis & Improve
System
Design
Integrate with Digital Twin & Test (MIL)
Integrate with ECU & Test (HIL)
Integrate with Physical Twin & Test (VIL)
Data analysis, System Verification & Improvement
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: V-model provides a structured framework for automotive development lifecycle
Advantage : Early verification avoids defects in later stages and saves cost

## Slide 14: Simulink Model for Automatic Emergency Braking (AEB)
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Dashboard
Sensor data from CARLA
Control commands to CARLA
AEB Logic

## Slide 15: Safety Analysis
    System-Theoretic Process Analysis (STPA)
    Why STPA ?
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
[Ref: New approaches for automated vehicles certification: Part I - current and upcoming methods for safety assessment]
Notes: STPA is a relatively new hazard analysis technique.
In addition to component failures, STPA assumes that accidents can also be caused by unsafe interactions of system components, none of which may have failed.
Hazards that were previously only found in operations can be identified early in development and both intended and unintended functionality are handled.

## Slide 16: System-Theoretic Process Analysis (STPA)
Identify Unsafe Control Actions
Identify Loss Scenarios
Define Safety Mechanism
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Safety Mechanisms for AEB
Communication:
Redundancy
Time out monitoring
Sensors:
Valid Range
Correlation
Control Actions:
Supervision and Correlation
[Ref: N. G. Leveson and J. P. Thomas, “STPA handbook”]
Notes: STPA is important due to loss scenarios

## Slide 17: Simulink Model for AEB with Safety Mechanisms
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Fault Injection & Warning Lamp
Backup Sensor Communication
Notes: The safety mechanisms are implemented in the model, A redundancy or back up if one sensor fails to send data.
A fault injection to create this loss scenario and a warning signal is sent if the system uses backup sensor.

## Slide 18: Model-in-the-Loop (MIL) Setup
Model-in-the-Loop test Setup
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: Explain What is model in the loop

## Slide 19: Safety Controller HY-TTC 580
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: rough operating conditions
ASIL C
high-end safety-control units

## Slide 20: Flashing the ECU using MOTAR
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Simulink Model
MOTAR Toolbox
Code Generation
Target ECU
Notes: configuring the simulink model into the MOTAR toolbox and the motar toolbox converts it into C code and generates a hex file which is then flashed into the target hardware.
This is how the AEB model is configured in the motar toolbox, the sensor inputs and control outputs are configured as per the CAN communication configuration defined according to the motar tool box.

## Slide 21: HIL Setup Communication
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: Now lets see how the total HIL setup communicates with each other.

## Slide 22: Simulink Model for CAN Communication
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
CAN Transmit
CAN Receive
CAN Configuration
Notes: This is the CAN communication model that acts as communication bridge between Carla and the ECU.
These are the sensor inputs from carla sent to the ECU.
This is the CAN configuration settings in simulink.
These are the control outputs received from the ECU and sent back to carla.

## Slide 23: Data analysis MIL vs HIL
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Collision
Collision
Notes: Higher speeds
Steeper brake curve
MIL and HIL results are similar
We can infer that as speed increases the obstacle is reached quicker and the braking becomes harsh leading to steeper braking curve.

## Slide 24: Results & Discussion
    Findings
    Limitations
    Challenges
    Computational Limitations
    Sensor Limitations
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: In Findings
virtual tests before physical tests
Reduce Testing costs
Accelerate Development Process
moving averages
by adding a delay in the Simulink model
Challenges – Thorough MIL and HIL tests for each system

## Slide 25: Conclusion
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
How a Digital Twin System can be integrated with a Safety Controller?
The Digital Twin setup interacts with Safety Controller via ROS and CAN and functions as intended.
1. How an Automotive System can be designed with Safety mechanisms?
Safety mechanisms were derived through STPA and implemented in the AEB system.
2. How can virtual sensors be used instead of physical sensors?
Virtual sensors from CARLA is used in the HIL simulation through DTS instead of physical sensors.
3. How a Safety Controller can be integrated into the HIL setup?
Safety Controller is integrated into the HIL setup by flashing the AEB model using MOTAR toolbox.
4. How the Digital Twin System’s performance can be optimized?
Data collected during the HIL testing can be used to optimize both the performance of Digital Twin and also the AEB system.
Notes: How it reduces the cost
Impacts on Industry and R&D
How digital twin improves testing
Faster test and development of algorithms

## Slide 26: Future Work
Model custom Maps
Model custom Cars
Custom Scenarios
Complete Physical Twin
Introduction
Problem Statement
Research Question
Methodology
Implementation
Results and Discussion
Conclusion
Future Works
Notes: Custom maps is currently a experimental feature in Carla’s Digital Twin update

## Slide 27
Thank you!
I would love to hear from you!
Questions?